## Slide 1
Sites Project: Topic Area Update Meeting
            California Department of Fish and Wildlife
            March 21, 2019

## Slide 2: What is the Sites Project?
2
  New large reservoir, regulating forebays, pipeline and Sacramento River diversion
    Fourteen miles long, 1.82 MAF storage
    Two 300’+ earthen dams, 9 saddle dams
    Two forebay regulating reservoirs connecting to existing irrigation canals
    14 miles of twin barrel, 12’ diameter pipelines and two pump/generation
    New 2,000 cfs diversion/pumping facility
  Sustainable Surface Water Infrastructure Improvement
    Benefits endangered species and refuges
    Increases water supply in drier years
    Reduce regional floods
    Increases recreation
    Is more effective with Climate Change
  Proposed by a local joint-powers authority. Participants throughout CA, Reclamation, State
Notes: Sites is a sustainable surface water project that uses available facilities and adds storage and conveyance to:
improve conditions for chinook salmon in drier years and delta smelt in all late-summers and falls
Increases deliveries to wildlife refuges in dry years
Eliminates floods that closed I-5
Increases water supplies for families, farms and business in drier years
Is more effective as climate changes occurs

## Slide 3: Regional Map

## Slide 4: Project Facilities

## Slide 5
Project Objectives
Primary:
Water Supply and Water Supply Reliability
Anadromous Fish Net Improvements
Operational Flexibility
Pelagic Estuarine Fish Net Improvements
Wildlife Refuge Supply
Secondary:
Hydropower
Recreation
Flood Damage Reduction

## Slide 6: Preliminary Design/Permitting Schedule
Permits & Water Right
Federal Authorizations (WIIN Act)
Rights of Way
Supplement
Draft EIR/S
Post Authorization Report
Final Feasibility Report
Federal WIIN Act
Application Review
Permit Planning & Applications
Preliminary Design & Geotech
Final Design
Construction
Early Ops
Prop 1 Ca Water Commission
Planning & permitting
Engineering & Rights of Way
Construction
operations
2019 Jan 01, Subject to Change
Early Funding
Mar 2019
Time Now
Jan 2018
Jan 2030
ROD, NOD, Permits, & Agreements
6
Encumber Prop 1
Funds
Jan 2020
Jan 2021
Jan 2022
Federal Deemed Feasible
Acquisition
EIR/S
Final
Notes: Pub.L. 114-322: 4007(i): Deemed feasible before Jan 1, 2021.
4013 Be in construction before 2021 Dec 16

## Slide 7: Previous Analyses
7
  Draft ER/EIS
    CalSim II (2010 DCR)
    DSM2, Upstream Water Temperature
    SALMOD, IOS
    Delivery assumptions vary for alternatives
  CWC WSIP Applications and Appeal
    CalSim II (2015) provided by DWR
    Unique Climate Change Assumptions
    DSM2, Upstream Water Temperature
    OBAN, SALMOD
    Delivery assumptions based on Alternative D
Notes: Sites is a sustainable surface water project that uses available facilities and adds storage and conveyance to:
improve conditions for chinook salmon in drier years and delta smelt in all late-summers and falls
Increases deliveries to wildlife refuges in dry years
Eliminates floods that closed I-5
Increases water supplies for families, farms and business in drier years
Is more effective as climate changes occurs

## Slide 8: Example Analyses Since DEIR and WSIP
  Sacramento Riverine Habitat Estimation
    Based on flood inundation – habitat mapping. Red Bluff to Knights Landing
    Nature Conservancy Habitat types
    HEC-RAS and GIS computation
  Hydraulic-limited river diversion limitations
    Stairstep limits to diversions based on SacRiver stage - flow
    Considers screen-pump limits at each location
    Reduces lower-flow diversions
  CalSim II merged model adding optional analysis of:
    CA Water Fix with variable diversion rates
    Freemont Weir notch
    Various climate change assumptions

## Slide 9: Daily Sacramento River Operations Modeling
  Provide information and help develop further understanding of the interaction of the proposed Sites Reservoir Project over a wide range of potential flow conditions in the Sacramento River.
  Assess potential ecosystem benefits of coordinated Sites operations
  Simulates daily flow conditions in the Sacramento River from Shasta Lake to Knights Landing
  Uses available historical gage records and reservoir operations records for period 1964 – 2018

## Slide 10: Flow Hydrograph Example

## Slide 11: Planned Analysis Tools
CalSim II – merged model with existing
USRDOM – expanded calibration and analysis to May 2018
Sacramento River HEC5Q model
American River HEC5Q Model
USBR Monthly Temperature Model
USBR early life stage mortality models
SALMOD
OBAN
IOS
DPM
DSM2 HYDRO, DSM2 QUAL, DSM2 PTM
Power models including LTGen, SWP Power and NODOS Power model
Economics Models including LCPSIM/CWEST, SWAP, LCRBQM and OMWEM
HEC-RAS for water surface change – habitat variation
CE-QUAL – W2 for Reservoir Water Quality

## Slide 12: Fish Screen Study Plan
Prepare a draft plan of study for evaluation of diversions to Sites Reservoir and potential impacts to fish survival associated with intake facility operations at the Red Bluff Pumping Plant, Hamilton City, and the proposed Delevan Intake.
Perform literature review
Identify information to establish biological baselines
Identify information to support permitting and development of performance criteria
Identify information to inform facility design
Identify pre- and post-construction monitoring and evaluation (M&E) requirements
Identify any long-term M&E requirements

## Slide 13: ESA Schedule:
Presidential Memo (10/19/2018)
Encourages Commerce and Interior to work together
  Streamline regulatory process
  In accordance with applicable law
Sites Project identified as major water project
Establishes schedule
  Joint biological assessment due to agencies in September 2019
  Biological Opinions by February 2020

## Slide 14: State Listed Terrestrial Species
Species | Federal Status | State Status
Foothill yellow-legged frog | No listing | Candidate, Threatened
Giant garter snake | Threatened | Threatened
Bald eagle | Delisted | Endangered
Swainson’s hawk | No listing | Threatened
Bank swallow | No listing | Threatened
Western yellow-billed cuckoo | Threatened | Endangered
Tricolored blackbird | No listing | Threatened
Greater Sandhill Crane | No listing | Threatened, Fully Protected
Palmate-bracted bird’s beak | Endangered | Endangered

## Slide 15: Mapping Approach
ICF is mapping land cover through aerial photo interpretation using
Google Earth
National Agricultural Imagery Program (NAIP) imagery
Topographic data obtained through LIDAR

## Slide 16: Terrestrial Species Models
Foothill yellow-legged frog | Perennial and intermittent streams with rocky substrates (not Sacramento River), Stone Corral Creek, Funks Creek (above reservoir), Antelope Creek
Giant garter snake | (Valley floor) AQUATIC - agricultural ditches, canals, freshwater emergent wetland, managed wetland, rice . UPLAND - areas within 200 feet of aquatic habitat that include annual grassland, other ag, disturbed, barren.
Western yellow-billed cuckoo | Riparian patches at least 25 acres in size
Swainson's hawk | NESTING - Riparian, other tree stands, isolated trees (not blue oak woodland); FORAGING - Minimum of 5-acre patches. Annual grassland, seasonal wetlands, alfalfa, hay fields, field crops, row crops, managed wetlands
Tricolored blackbird | NESTING - emergent marsh, managed wetland, riparian (blackberry thickets) FORAGING - annual grassland, seasonal wetland, grain/hay crops, field crops, rice, fallow
Bald eagle | NESTING - Riparian, FORAGING - Reservoir, river

## Slide 17: WSIP Process Lessons Learned
What we thought
Sites = cold water pool management = climate resiliency = anadromous fish benefits
What we learned
Need to revisit benefits to salmon populations
Collaboration with regulatory agencies is essential
Benefit of pulse flow to Yolo Bypass for delta smelt acknowledged
Benefit to refuge water supply acknowledged

## Slide 18: Approach to Biological Assessment
The Challenge:
Given flexibility created by off-stream storage for management of cold water pool and flows;
How do we build and operate the project to provide a net benefit to fishery resource?
We would like to work with CDFW, NMFS, and USFWS to develop an approach to weigh benefits and impacts of operations
And develop an operations plan that is expected to achieve a net benefit to the environment

## Slide 19
Near-Field Effects Analyses
Salmonids:
Spatial distribution (horizontal/vertical: literature review, with specific info. for water surface elevations of screens, etc.)
Entrainment (size distribution)
Impingement/screen contact/passage time (literature review & Swanson et al. analyses)
Predation (literature review, incl. Vogel GCID studies)
Stranding behind overtopped screens (high flow, based on water surface elevation)
Green Sturgeon:
Review of protective velocity criteria and timing (Verhille et al. 2014)
Entrainment (size distribution)

## Slide 20
Far-Field Flow-Survival Analysis
Juvenile Chinook Salmon:
Proposing to use model from new Henderson et al. (2018) paper
Peer-reviewed (CJFAS)
Multiple reaches from above Red Bluff down to Knights Landing
Focus on Sites withdrawal period (winter/spring), daily timescale
Incorporates flow and temperature effects
Also includes other (non-operations) covariates
Results will allow adjustment of other models, e.g., OBAN

## Slide 21
Life Cycle Modeling
OBAN:
Winter-Run Chinook Salmon
July-Sep temp. (eggs/alevins)
Aug-Nov flow (fry)
Dec-Mar Yolo flow (juveniles)
Dec-Jun exports (juveniles)
DCC (Dec-Mar) (juveniles)
Adjustment of Sac. R. migration survival per Henderson et al. results
Ocean conditions not affected by project but included in model (productivity and harvest)

## Slide 22
Effects to Delta Species
Delta Smelt
Fall X2 habitat (Feyrer et al. 2011)
Adult and larval entrainment (Grimaldo et al. 2009; Grimaldo et al. 2017)
Later summer/fall flows carrying food (IEP Studies)
Sediment entrainment by Project intakes
Longfin Smelt
Juvenile abundance vs winter-spring outflow (Kimmerer et al. 2009
Stock-recruit dynamics (Nobriga and Rosenfield 2016)
Adult and juvenile entrainment (Grimaldo et al. 2009)